## Slide 1
Emergency Evacuation
Spring 2018 EECS 372
Multi-Agent Modeling
Professor Uri Wilensky
Eric Hao
Motivation
  It impacts real lives during emergencies
  Agent-Based Modeling (ABM) can be applied naturally and intuitively
  Applications extend beyond emergency readiness, including computer vision and swarm intelligence
Emergent Behaviors
  People clog around exits, forming a circular crowd around the exit:
  People who cannot see exits or do not know where exits are try to follow the direction of the crowd, creating a herding or flocking behavior:
How It Works
  At each tick, each person selects a target
    Select a visible exit. If there are none, then
    Select a visible checkpoint. If there are none, then,
    Select a nearby visible spot
  Selection is based on five heuristics
The Five Heuristics
  Crowdedness: How crowded is it?
  Wall proximity: How many walls are near it?
  Distance from me: How far away is it from me?
  Distance from exits: How far away is it from exits?
  Crowd heading: Is the crowd heading toward or away from it?
Heuristic Selection
Heuristic selection is handled differently when choosing different types of targets (exits, checkpoints, or regular patches). This is because the desirability of the heuristics varies depending on what type my target is. For example, if I am picking an exit, crowdedness is bad. However, if I don’t see any exits, then crowdedness is good.
Sensitivity Analysis
  Three parameters were tested against number of people
    Door proximity (how close together exits are)
    Hallway width
    Number of rooms
Results
Having exits very close together increases evacuation time, because the crowds around two exits merge into an even larger one. Exits far apart are bad, too, because redistribution between exits takes longer. Larger hallways are better when there are not that many people (over 100), but it either doesn’t matter or might even be slightly worse when there are lots of people (under 100). In general, more rooms are better, except when there are fewer (50) people in the room.
Chart: Evacuation Time and Door Proximity
| 1 | 3 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27
25 | 81.24 | 80.52 | 79.24 | 81 | 78.48 | 78.36 | 79.44 | 77.6 | 78.04 | 79.08 | 77.96 | 75.88 | 79.6 | 79.84
50 | 83.6 | 83.16 | 81.96 | 82.48 | 81.96 | 83.68 | 82.64 | 83.2 | 82.08 | 84.36 | 83.52 | 83.04 | 84.12 | 83.2
100 | 115.24 | 110.24 | 103.44 | 100.4 | 99.72 | 100.2 | 101.08 | 101.64 | 102.76 | 105.2 | 104.56 | 105 | 104.32 | 102.88
150 | 167.08 | 155.44 | 142.48 | 140.84 | 139.36 | 140.56 | 139.52 | 140.92 | 142.44 | 140 | 144.16 | 143.16 | 146.76 | 145.16
200 | 215.6 | 201.4 | 189.44 | 183.4 | 180.96 | 182.08 | 181.84 | 182.88 | 184.28 | 183.12 | 182.72 | 187.24 | 186.96 | 190.28
250 | 267.08 | 248.56 | 232.04 | 226.64 | 223.32 | 224.56 | 224.16 | 225.48 | 225.52 | 225.32 | 228.64 | 228.6 | 229.76 | 228.68
Chart: Evacuation Time and Hallway Width
| 3 | 5 | 7 | 9 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31
25 | 99.6 | 100.8 | 97.44 | 98.36 | 93.68 | 92.48 | 91.8 | 89.6 | 87.76 | 87.08 | 84.84 | 83.56 | 82.28 | 82.48
50 | 109.32 | 107.64 | 106.36 | 104.8 | 103.92 | 101.24 | 102 | 100.92 | 100.8 | 101.12 | 100.6 | 98.84 | 101.84 | 100.72
100 | 182.76 | 183 | 180.64 | 183.4 | 180.72 | 180.76 | 182.48 | 180.36 | 182.08 | 181.12 | 184.8 | 183 | 179.84 | 182.72
150 | 262.88 | 266.04 | 266.92 | 264.56 | 268.04 | 266.48 | 264.08 | 268.24 | 266.92 | 268.04 | 268.92 | 270.24 | 266.56 | 265.44
200 | 348.56 | 352.48 | 355.44 | 351.88 | 353.24 | 350.84 | 353.16 | 356.92 | 352.04 | 353.24 | 354.28 | 356.72 | 354.64 | 352.2
250 | 435.04 | 432.6 | 440.52 | 441.6 | 441.16 | 438.16 | 439.84 | 443.96 | 440.44 | 438.92 | 440.4 | 441.52 | 444.4 | 439.4
Chart: Evacuation Time and Number of Rooms
| 2 | 4 | 6 | 8 | 10
25 | 95.68 | 97.12 | 95.16 | 98.96 | 98.04
50 | 128.92 | 112.6 | 108.32 | 106.6 | 106.32
100 | 204.28 | 191.44 | 185.44 | 183.72 | 182.96
150 | 284.64 | 273.08 | 270.28 | 267.88 | 266.28
200 | 361.5833 | 354.24 | 355.72 | 354.2 | 355.32
250 | 455.24 | 440.04 | 443.56 | 436.16 | 437.52